## Slide 1: Design Review: CGRA 3D PnR Using Nanoelectromechanical Relays
October 30th, 2020
Michael Oduoza

## Slide 2: Section 1
Background and motivation

## Slide 3: CGRA
 | Processing Element
 | (PE) / Compute
 | Memory (MEM)
 | Switch box (SB)
 | Connection box (CB)
MEM
MEM
MEM
MEM
PE
PE
PE
PE
PE
PE
PE
PE
MEM
MEM
MEM
MEM
Coarse Grained Reconfigurable Array (CGRA)
Tile
Notes: CGRA is an array of PE tiles, whereby each PE tile consists of one Processing element, and some switch boxes and connection boxes. These PE tiles are all connected through routing tracks, which are the wires shown in blue. This is where most of the reconfigurability overhead comes from.

## Slide 4: Single PE Tile
Chart: PE Tile Area Breakdown
| Connection boxes (1 bit) | Connection boxes (16 bit) | Switch box (1 bit) | Switch box (16 bit) | Processing element | Other
 | 892.054 | 717.772 | 883.235 | 4086.482 | 2870.734 | 367.971

## Slide 5: Concept – 3D PnR with NEM Relays

## Slide 6: Multipole NEM Relay
Gate

## Slide 7: Multipole NEM Relay

## Slide 8: 3D PnR with NEM Relays
NEM Relay process flow compatible with standard CMOS BEOL flows
Allows for 3D integration

## Slide 9: Section 2
NEM Relay-mux mapping

## Slide 10: Mapping a Mux to Relay Switches
Similar to pass-gate logic

## Slide 11: Connection Box - 16 bit

## Slide 12: Switch Box - 16 bit

## Slide 13: Table of Potential Mappings
Module | Type of Mux | # of Mux Occurrences in Module | # of Module Instantiations in PE Tile
16-bit CB | 10-to-1 | 1 | 2
1-bit CB | 14-to-1 | 1 | 4
16-bit SB | 2-to-1 | 20 | 1
16-bit SB | 4-to-1 | 20 | 1
1-bit SB | 2-to-1 | 20 | 1
1-bit SB | 4-to-1 | 20 | 1

## Slide 14: Section 3
NEM Relay mux layouts

## Slide 15: Design Hierarchy
M10 – Relay Gate, S/D
M9 – Horizontal Routing
M8 – VSNEM; Vertical Routing
M7 – VDD; VSS
M6 – VDD; VSS
M5-M1
NEMBODY, NEMCHAN, etc.
VSNEM = -2.6V;

## Slide 16: Metallization Hierarchy
M8, M9 will have same lithographic characteristics as M1, M2, etc.
To allow for dense routing in NEM mux layers (next slide)

## Slide 17: 2-to-1 Mux, 16 bit
Design Challenges/Notes
All pins in M7 (except VSNEM in M8)
Neighboring relays share body connection
Very dense layout
    Can’t run metal lines directly over S/D regions
    Need to lead output pins away, then run horizontal z-lines across relay
Need to keep signal pins away from power rails
    Don’t want via stack to run into M7/M6 VDD/VSS rails on the way down
NEM Relays need to “click into NEM relay sites” on chip (in between VSNEM rails)
    Pitch of VSNEM rails chosen carefully
    Pitch of VDD/VSS lines chosen carefully
NOTE: These layouts were done manually!
Notes: Explain signals, power, etc. Why are pins led away? Why is power rail so fat?

## Slide 19: 2-to-1 Mux, 16 bit (continued)

## Slide 20: 4-to-1 Mux, 16 bit

## Slide 21: 4-to-1Mux, 16bit (continued)

## Slide 22: 16-to-1 Mux, 16 bit
Design Challenges/Notes
16-to-1 mux, but don’t want long and skinny macro…
    Stack 16-bit pairs on top of each other and route output nodes vertically, as well as horizontally
    Jogs needed for vertical lines (to avoid obstacles)
    Nearly all lines are min. width and min. spacing
Routing power (VSNEM) and signals in the same layer – could potentially cause coupling issues (will do analysis later)
Potentially large wire load capacitance seen at input and output pins
    May increase delay
    PnR tool may need to insert buffers (Area!)
    Will analyze in PD flow
NOTE: These layouts were done manually!
Notes: Explain how layout is organized I0 (0-7) I1 (0-7) I0 (8-15) I1 (8-15)

## Slide 24: 16-to-1 Mux, 16 bit (continued)

## Slide 25: 4-to-1, 1 bit example

## Slide 26: Section 4
Preliminary area analysis

## Slide 27: Area Analysis
CMOS Layer
NEM Layer
Required Chipcore area = max{CMOS Area, NEM Area}

## Slide 28: Concept - Favorable 3D Place and Route
CMOS Layer
NEM Layer
Required Chipcore area = max{NEM Area, CMOS Area}
Total chipcore area is reduced
CMOS-only implementation

## Slide 29: Concept - Unfavorable 3D Place and Route
CMOS Layer
NEM Layer
Required Chipcore area = max{NEM Area, CMOS Area}
Area increase If NEM Area > original chipcore area!
CMOS-only implementation
Notes: Either this or the CMOS layer is too large due to buffers

## Slide 30: NEM Relay vs. CMOS Size
NEM Relay pitch is 4um
Area = 4um x 4um
Much larger than CMOS std. cell area.
NEM relay cost must be amortized over a large # of stdcells.
NEM Relay
CMOS std. cell

## Slide 31: Area Benefit (or penalty) Estimate
Relay pitch is 4um
0.3 um extension at each edge
Each NEM relay mux has “L” rows (of relays) and “W” cols (of relays)
Let “N” be total # of muxes in module
NEM-MUXarea = N * [(L * 4 um + 0.6um) * (W * 4um + 0.6um)]
    Compare this to data on CMOS-only area for each SB, CB module

## Slide 32: Area Benefit (or penalty) Estimate

## Slide 33
CMOS-only implementation

## Slide 34
CMOS-layer
NEM Layer

## Slide 35
CMOS-layer
NEM Layer

## Slide 36
CMOS-layer
NEM Layer
Optimum Point

## Slide 37
CMOS-layer
NEM Layer
Unfavorable 3D place and route!

## Slide 38: Relay vs. CMOS 3D PnR Tradeoff
Area
# of muxes mapped to relays
Total NEM layer area
Total CMOS layer area
Area CMOS bound
Area relay bound
Optimal operating point

## Slide 39: Relay vs. CMOS 3D PnR Tradeoff – Implications
Not all muxes will be mapped to relays
E.g. In switch box where we have both 4:1 and 2:1 muxes
    Consider mapping just the 2:1s
    More analysis to come
  Single-bit connection box (14:1) is out of the question (will stay in CMOS layer)

## Slide 40: Section 5
3D Pnr flow: preliminary results + future plans

## Slide 41: PD Update
Design Challenges/Notes
“Tricked” the PnR tool into doing a 3D place and route
PnR tool has a hard time with power routes
    End up with shorts and open power nets if job left to PnR tool
  Manual floorplan of macros required
July 2020
September 2020

## Slide 42: End
Thanks for listening! Questions?